Engineering Specification

Model F1 Series Standard Response Automatic Sprinklers

Recommended CSI MasterFormat Specification Location: 21 13 00, Fire Suppression Sprinkler Systems (formerly 13930)

Sprinklers shall be a standard response, [standard spray upright] [standard spray pendent] [standard spray recessed pendent] [conventional upright/pendent] [vertical sidewall] [horizontal sidewall] [recessed horizontal sidewall] that is [cULus Listed] [FM Approved]. Sprinkler frame and deflector shall be of bronze frame construction having a ½” NPT thread.  Water seal assembly shall consist of a Teflon-coated Belleville spring washer and top-loaded extruded cup with 5 mm glass bulb containing no plastic parts. Sprinkler temperature rating shall be [135F (57C)] [155F (68C)] [175F (79C)] [200F (93C)] [286F (141C)] [360F (182C)] [500F (260C)]. Sprinklers shall have a nominal K-factor of [2.8 gpm/psi1/2 (40 l/min/bar1/2) – small orifice] [4.2 gpm/psi1/2 (61.0 l/min/bar1/2) – small orifice] [5.6 gpm/psi1/2 (81.0 l/min/bar1/2) – standard orifice]. Sprinklers shall have a rated working pressure of 175 psi (12.1 bar).  Standard finish: [Bronze] [Chrome Plated] [Polyester Coated] [Special finish– specify].

Sprinklers shall be of the Model F1 Series. Refer to Reliable Bulletin 013 for associated sprinkler identification number (SIN) with respect to style, orifice size and thread combination.

For recessed sprinklers, add:

{Recessed escutcheon assembly shall be a two-piece “friction fit” escutcheon with [Model F2 escutcheon: ½” (13 mm)] [Model F1 escutcheon: ¾”(19 mm)] adjustment.} {Pendent sprinklers only: Recessed escutcheon assembly shall be a factory-assembled, two-piece steel escutcheon of push-on/thread-off design with ½” adjustment. Standard finish shall be [White Painted] [Chrome] [Brass] [special finish – specify]}

Standard finish: [White Painted] [Chrome] [Brass] [Special finish– specify].

Recessed escutcheons that are permitted by the manufacturer to be used with each Model F1 Series recessed sprinkler shall be used.