Engineering Specification

Model F156-300 Series Standard Response Automatic Sprinklers

Recommended CSI MasterFormat Specification Location: 21 13 00, Fire Suppression Sprinkler Systems (formerly 13930)

Sprinklers shall be a standard response, standard spray [upright] [pendent] that is cULus Listed. Sprinkler frame and deflector shall be of bronze frame construction having a ½” NPT thread. Water seal assembly shall consist of a Teflon-coated Belleville spring washer and top-loaded extruded cup with 5 mm glass bulb containing no plastic parts. Sprinkler temperature rating shall be [135F (57C)] [155F (68C)] [175F (79C)] [200F (93C)] [286F (141C)] [360F (182C)]. Sprinklers shall have a nominal K-factor of 5.6 gpm/psi1/2 (81 l/min/bar1/2) – standard orifice. Sprinklers shall have a rated working pressure of 300 psi (20.7 bar). Standard finish: [Bronze] [Chrome Plated] [White Polyester] [Special finish– specify].

Sprinklers shall be of the Model F156-300 Series. Refer to Reliable Bulletin 025 for associated sprinkler identification number (SIN) with respect to style, orifice size and thread combination.

For recessed pendent sprinklers, add:

{Recessed escutcheon assembly shall be a factory-assembled, two-piece steel escutcheon of push-on/thread-off design with ½” (13 mm) adjustment. Standard finish: [White Painted] [Chrome] [Brass] [Special finish – specify].} {Recessed escutcheon assembly shall be a two-piece “friction fit” escutcheon with [Model F2 escutcheon: ½” (13 mm)] [Model F1 escutcheon: ¾”(19 mm)] adjustment. Standard finish: [White Painted] [Chrome] [Brass] [Special finish– specify].}

Recessed escutcheons that are permitted by the manufacturer to be used with each Model F156-300 Series recessed sprinkler shall be used.