Engineering Specification

Model F1FR-300/CCP

Quick Response Concealed Sprinkler

Sprinklers shall be [cULus Listed] [NYC MEA Approved – 258-93-E] quick response, concealed pendent sprinklers.  Sprinkler frame and deflector shall be of bronze frame construction having a ½” NPT thread, with brass cover plate and copper alloy retainer flange assembly.  Water seal assembly shall consist of a Teflon-coated Belleville spring washer and screw machined brass cup with 3 mm frangible glass bulb containing no plastic parts.  Sprinklers shall have a nominal K-factor of[5.6 (81.0). Sprinkler temperature rating shall be [135 (F (57 (C)] [155 (F (68 (C)] [175(F (79 (C)] [200 (F (93 (C)] with a cover plate temperature rating of [135 (F (57 (C)] [165 (F (74 (C)].  Method of attaching the cover plate to the factory-assembled, steel sprinkler cup shall be a push-on and thread-off design allowing  [½” (13 mm)] [5/16” (8 mm)] of adjustment.  Rated working pressure shall be 300 psi (20.7 bar).  A factory applied protective cap shall be provided to protect against installation damage.  Standard cover plate finish to be:  [Chrome] [White] [Specialty – specify]. Quick Response extended coverage concealed sprinkler shall be Reliable Model F1FR-300/CCP, SIN R5615 (Bulletin 164).