Engineering Specification

Model G Check Valve

Recommended CSI MasterFormat Specification Location: 21 13 00, Fire Suppression Sprinkler Systems (formerly 13930)

Check valves shall be [cULus Listed] [FM Approved] for use in wet-pipe or dry-pipe fire protection systems for installation in the vertical or horizontal position.  Check valve construction shall be cast iron with bronze seat with a straight flow design, spring loaded type. Check valve size shall be [1½” (40mm)] [2” (50mm)] [2½” (65mm)] [76mm] [3” (80mm)] [4” (100mm)] [6” (150mm)] [165mm] [8” (200mm)] [10” (250mm)] with grooved end connections per ANSI/AWWA C606.  The check valve shall be provided with ½” NPT (R½) connections on both the supply side and the discharge side.  The check valve shall have a rated working pressure of [300 psi for nominal sizes 1½” (40mm) through 2” (50mm)] [250 psi for nominal sizes 2 ½” (65mm) through 8” (200mm)] [300 psi for nominal size of 10” (250mm)].

Check valve shall be the Reliable Model G swing check valve. Refer to Reliable Bulletin 807 for associated information.